Fire Extinguisher Training

# Text boxes

Pull the pin – Test the fire extinguisher to make sure it works

Aim the extinguisher at the base of the fire

Squeeze the handle to activate the fire extinguisher

Sweep across the base of the fire from side to side until agent blankets or cools the fire.

Fire Extinguisher Inspections

- Type and Pressure Gauge

Fire Extinguishers

Campus Locations

- P/W (Pressurized Water)

- 30’ for ~ 1 minute

- Residence Halls

- ABC (Dry Chemical)

- 15’ for ~ 30 seconds

- Kitchen/Laboratory/Vehicle

- CO2  (Carbon Dioxide)

-   5’ for ~ 15 seconds

- Electrical/Lab/Mechanical

- K      (Acetic Acid/Vinegar)

- 10’ for ~ 30 seconds

- Schwems and Valentine

- Metl-X

- Laboratory

Fire Tetrahedron

- All 4 must be present to have a fire

- Remove any one of the 4…Fire goes out

Fire Classifications

- A – Ash producing materials

- B – Liquids found in a Barrel

- C – Circuit or Current

- D – Dangerous Metals

- K – Kitchen Cooking Equipment

Fire and/or Smoke Condition

- If a fire is discovered, follow the Amherst College Emergency Procedures, regardless of whether or not you can control the incident

- Evacuate / Extinguishment

- Never use a fire extinguisher unless you have been trained and it is safe to do so.

- Lack of training, or the use of the 	wrong extinguisher could result in 	fire spread or serious injury.